## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: LCA Requirements and Guidelines: ISO 14044
Module A2
It is suggested to review Module A1 prior to this module

## Slide 4: Disclaimer on this Module
The standard can be purchased from a few sources: ISO ANSI Other standard organizations
This module intended only as an overview of ISO 14044 by the International Organization for Standardization. It does not include all of the information in that standard and presentation of the information is subject to our interpretations. Therefore, this module is not meant as a replacement for reading the standard when carrying out an ISO compliant LCA, but simply as an introduction to the general requirements.

## Slide 5: ISO 14044:2006 Background
LCA Requirements and Guidelines
Similar to ISO 14040 in:
  Introduction
  Terminology definitions
  Phases and overview of process
Describes in more detail the required process for completing a life cycle assessment
First and only edition published in 2006
Replaces a host of previous ISO LCA standards

## Slide 6: ISO LCA Standards Combination
ISO 14040:2006
Principles and Framework
ISO 14044:2006
Requirements and guidelines
ISO 14040:1997
Principles and framework
ISO 14041:1998
Goal and scope definition and inventory analysis
ISO 14042:2000
Life cycle impact assessment
ISO 14043:2000
Life cycle interpretation

## Slide 7: Phases of an LCA
Image Sources: Target: wikia.nocookie.net Data: dreamstime.com Earth: business2community.com

## Slide 8: LCA Phases
Goal statement is the first component of an LCA and guides much of the subsequent analysis
Goal must state:
Intended use
Reasons for study
Audience
Whether comparative and disclosed to public
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation
Goal Statement

## Slide 9: LCA Phases
Function and functional unit
  Define the functional characteristics of the product system
  Functional unit for amount of function achieved, useful as a reference measure
System boundary
  Define which processes are included in the study
  Helpful to include a process flow diagram
LCIA methodology
  State which impact categories and category indicators are used
  State which impact characterization methodology is used
Inventory Data
  Obtain either from direct measurement of processes or from secondary sources (or a mix of the two)
  Include inputs and outputs to air, water, and soil
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation
    All developed to be consistent with the stated goal of the LCA
Scope Elements

## Slide 10: LCA Phases
Data quality
  Address age, geographic coverage, technology coverage, precision, completeness, representativeness, consistency, reproducibility, sources, minimum length of time to collect, and uncertainty.
  For missing data a zero value, non-zero value, or a calculated value from similar technology should be used and explained.
Comparisons between systems
  Use the same functional unit, system boundaries, data quality, allocation, and impact assessment procedures (if not possible, identify differences)
  For publicly disclosed studies must include a critical review and the LCIA phase
Critical Review
  State whether or not a critical review will be conducted
  Define how, and by whom, the critical review will be carried out
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation
    All developed to be consistent with the stated goal of the LCA
Scope Elements (cont.)

## Slide 11: LCA Phases
Collect for each unit process and reference sources, time taken, quality, etc.
Clearly define each unit process to prevent overlap in data collection
Provide the following details:
  Overall process flow diagrams
  Description of each unit process with inputs and outputs
  Flows and operating conditions of each unit process
  Units used
  Description of data collection techniques
  Instructions to document irregularities and all details
Example data collection sheet provided in the standard
Data Collection
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation

## Slide 12: LCA Phases
Collect data and classify under the following major headings
Energy inputs, raw material inputs, ancillary inputs, and other physical inputs
Releases to air, water, and soil
Products, co-products and waste
Other environmental aspects
Data Classifications
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation

## Slide 13: LCA Phases
Consider goal and scope
Prepare for data collection
Collect data
Validate data
Relate data to unit process and allocations (reuse, etc.)
Relate data to functional unit
Aggregate data
Refine system boundary
Revise, repeat as needed
Data Collection Procedure
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation
Already done if using database
Already done if data from literature

## Slide 14: LCA Phases
Data are converted into potential environmental impacts
During LCIA determine if:
  Quality of data sufficient to conduct the LCIA
  System boundaries and cut-offs (magnitude of input or output flow that is small enough to be negligible) appropriate to calculate indicator results
  Other methodological choices, like the choice of functional unit or averaging used, decreased the direct linkage between the data collected and environmental impact results obtained, potentially biasing the results
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation
Life Cycle Impact Assessment

## Slide 15: LCA Phases
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation
Mandatory Elements
Mandatory Elements
Classification
Impact category selection (Comprehensive set)
Characterization
Characterization model selection (impact methodology)
Category indicator selection

## Slide 16: LCA Phases
Impact category selection:
  GWP, AP, EP, ETP, HHNCP, HHCP HHCAP, ODP, SCP
Category indicator selection:
  kg CO2-eq for GWP, kg SO2-eq for AP, kg N-eq for EP, etc…
Characterization model selection:
  TRACI 2.1* (other options include IMPACT 2002+, eco-indicator 99, CML 2001…)
Classification:
  NH3 (Ammonia)  Acidification, HH Particulates, Eutrophication
Characterization:
  Acidification:
  Particulates:
  Eutrophication:
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation
Mandatory Elements Example
Repeat for each flow, sum results in each impact category
Characterization factor
*TRACI is the Tool for the Reduction and Assessment of Chemical and Other Environmental Impacts

## Slide 17: LCA Phases
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation
Optional Elements
Optional Elements
Normalization
Weighting
Grouping
Data Quality Analysis
These elements can be useful to help decision makers interpret results, but also may introduce additional subjectivity. Inclusion of these elements should be consistent with goal and scope.
Notes: Data Quality Analysis includes
  Gravity analysis such as Pareto analysis identifies data with the greatest contribution
  Uncertainty analysis
  Sensitivity analysis

## Slide 18: LCA Phases
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation
Example of terminology for acidification
Impact Category
Acidification potential
LCI result
500 kg SO2, 100 kg NOx , 10 kg HNO3 per functional unit
Characterization Model
TRACI 2.1*
Characterization Factor
Category Indicator Result
Category Indicator
Increase in acidity in the environment (moles H+)
Potential of each compound to cause acid deposition (such as acid rain) in relation to that of SO2
Kilograms of SO2-equivalent
Category Endpoints
Environmental Relevance
Ecosystem effects such as acidic lakes, corrosion to buildings, damage to plants
Increased emissions of species such as nitric oxides and sulfur oxides directly contribute to increases in environmental acidity, depending on transport and chemistry models, such as in the form of acid rain.
*TRACI is the Tool for the Reduction and Assessment of Chemical and Other Environmental Impacts

## Slide 19: LCA Phases
No weighting allowed
Sufficiently comprehensive set of category indicators
Category indicators should be scientifically valid, environmentally relevant, and internationally accepted
Not sole basis for decisions
Must include sensitivity and uncertainty analyses
If grouping used then there are lots of additions (caveats) required as in Section 5.3.2
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation
Comparative Assessment LCIA

## Slide 20: LCA Phases
Identify significant issues with:
  Inventory data
  Impact categories
  Significant contributions from life cycle stages
Include information on:
  Assembled findings from LCI and LCIA
  Methodologies used
  Value choices
  Limitations
  Roles of interested parties in compilation and review
Consider the following that may be critically reviewed:
  Completeness check
  Sensitivity check
  Consistency check
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation
Interpretation
Takes the form of conclusions and recommendations
Notes: Completeness check is making sure all relevant data all data needed for a sound interpretation was included
Sensitivity check is examining how much uncertainty might have affected results
Consistency check is making sure that the assumptions, methods, and data were consistent with the stated goal and scope

## Slide 21: LCA Phases
Process intended to ensure consistency between a life cycle assessment and the principles and requirements of the lnternational Standards on life cycle assessment*
Done by an independent third party
Defined in the scope
Required if comparative and disclosed to the public
All LCA phases might be critically reviewed, with the exception of the goal
Answers the questions in the following slide
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation
Critical Review
*ISO 14044
Notes: Completeness check is making sure all relevant data all data needed for a sound interpretation was included
Sensitivity check is examining how much uncertainty might have affected results
Consistency check is making sure that the assumptions, methods, and data were consistent with the stated goal and scope

## Slide 22: Responsibilities of Critical Review
Methods consistent with ISO 14044?
Methods scientifically and technically valid?
Data appropriate and reasonable for scope?
Interpretations reflect limitations and goal?
Study is transparent and consistent?

## Slide 23: Thank you for completing Module A2!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules
Please remember that this presentation is not intended as a replacement for reading ISO 14044 when carrying out an LCA.

## Slide 24: Self-Assessment Quiz
MODULE A2: ISO 14044

## Slide 25: What is the first step of the data collection procedure?
Collect data
Refine system boundary
Consider the goal and scope

## Slide 26: Correct!
Since all procedures need to be consistent with the goal and scope, this is generally the first consideration when starting any process in LCA

## Slide 27: What is the difference between ISO 14040 and ISO 14044?
ISO 14040 is the general introduction to life cycle assessment concepts and procedures, while ISO 14044 includes more details about the procedures.
ISO 14040 describes life cycle assessment procedures, while ISO 14044 is an example of a life cycle assessment.
ISO 14044 is the updated version of ISO 14040

## Slide 28: Correct!
ISO 14044 simply gives more detail-oriented guidance about the specific procedures for completing an LCA

## Slide 29: Which of these is an optional element of the LCIA phase?
Grouping
Classification
Characterization
None of the above

## Slide 30: Correct!
Grouping, weighting, normalization, and additional quality analysis are all optional steps of the LCIA phase.

## Slide 31: Can the Goal and Scope be updated after completing the LCI stage?
No, it must be left as originally written
Yes, but it should be avoided if possible
Yes, this type of iterative process is encouraged and can strengthen results

## Slide 32: Correct!
The entire process of life cycle assessment is iterative between each phase to accommodate incorporation of new information at any point.

## Slide 33: Sorry that’s Incorrect
Please try again!