## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: Building LCA Software Tutorial (BIRDS, BEES)
Module γ2

## Slide 4: Building Industry Reporting and Design for Sustainability (BIRDS v1)
For environmental and economic analysis of new commercial buildings
  Operating energy
  Environmental performance of materials, construction, and use
  Life-cycle cost
Online-based tool
Produced by NIST in the US
Simple input in three steps (output options in fourth step)
  Select building
  Select comparisons
  Select environmental preferences
Available at: birdscom.nist.gov
Logo: birdscom.nist.gov

## Slide 5: BIRDS (Step 1)
Building types include
  Apartment
  Dormitory
  Hotel
  Office
  Restaurant
  Retail Store
  High School
For each various number of floors available
Click to open detailed information as shown

## Slide 6: Baselines
In Steps 2 and 3 baselines must be selected including
  Building location
  Building energy standard
  Study period
  Impact category weighting scheme
In Step 4, will choose which to make comparisons along
Only one can be used as the basis of comparison at a time
All others will take value of base case

## Slide 7: BIRDS (Step 2)
ASHRAE 189.1-2009
Choose baseline value
  State
  City
  ASHRAE Edition
  Time period (1-40 years)
Can choose alternatives to compare to
  Same selections as baseline
ASHRAE 90.1
  Energy Standard for Buildings Except Low-Rise Residential Buildings
  Prescriptive or performance based
  Often used as municipal/state standard or part of standards

## Slide 8: BIRDS (Step 3)
12 impact categories
Choose weighting scheme
  BEES Stakeholder Panel
  EPA Advisory Board
  Carbon Footprint Only
  Equal Weights
  Custom Weights
This baseline and alternatives is not referring to baseline/ alternatives chosen in Step 2
  Just alternative weighting schemes to apply to all cases
Click by Pre-defined Weights to see how schemes are developed

## Slide 9: BIRDS (Step 3)

## Slide 10: BIRDS (Step 4)
Indictor unit
  kg eq substance
  kg eq substance/ft2
  change in each
Choose one dimension as comparison basis
  Building location
  Building energy standard
  Study period
  Impact category weighting scheme
Choose type of results
  Life-cycle cost
  Operating energy
  Environmental impact

## Slide 11: BIRDS Results Study Period Global Warming kg CO2-eq
Shows total impact (not yearly)
Divide by study period for yearly impact
Shows only selected unit on chart
  All units in table below

## Slide 12: BIRDS Results Locations All (Weighted) Env. Impact Score

## Slide 13: BIRDS Results Energy Edition Smog kg O3-eq/ft2

## Slide 14: Building for Environmental and Economic Sustainability (BEES)
Predecessor to BIRDS
For environmental and economic analysis of building products
Online-based tool
Produced by NIST in the US
Analyze individual building products (rather than whole building)
Nearly 200 products included
  Concrete, roofing, insulation, water distribution piping, cleaning materials, paving, more
Simple to use
  Most data and processes set, just choose weighting scheme, product(s) of interest, and transport distance
Link to BEES online

## Slide 15: BEES Analysis Parameters

## Slide 16: Environmental Weighting Scheme

## Slide 17: Performance weights
BEES can output a “score” in addition to impact category indicators
This weights importance of environment and economics in scores
For environmental analysis alone, enter 100
Discount rate deals with time value of money (does not affect environmental)
  1 dollar invested today might be worth 2 dollars in 10 years

## Slide 18: Element Selection
Major group elements include
  Building Maintenance
  Building Repair & Remodeling
  Building Sitework
  Domestic Water Distribution
  Equipment & Furnishings
  Interiors
  Sanitary Waste
  Services
  Shell
  Substructure
All products in one list

## Slide 19: Product Selection
Inventory results by life cycle stage
Only appears after clicking compute

## Slide 20: Output Type Selection

## Slide 21: BEES Output
By life cycle stage
By environmental flow

## Slide 22: Thank you for completing Module γ2!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules